Overview
ALICE FMD Calibration Considerations
Overview
The FMD
FMD Calibration classes
AliFMDParameters
DCS `Conditions' DB
Calibration Procedures
Status
Christian Holm Christensen
[Speaker Notes: Next, the pedestal and gain calibrations are read in to translate ADC counts to energy deposition and charge particle multiplicity in each active strip.]

---
ALICE FMD Calibration Considerations
The FMD detector:
Silicon strip sensors
3 subdetectors ...
... with each 1 or 2 rings
51200 channels
[Speaker Notes: Next, the pedestal and gain calibrations are read in to translate ADC counts to energy deposition and charge particle multiplicity in each active strip.]

---
Calibration Classes
FMD Calibration Data Classes
TObject
AliCDBEntry
AliFMDId
#fDetector: UShort_t
#fRing: Char_t
#fSector: UShort_t
#fStrip: UShort_t
AliFMDCalibGainEntry
#fValue: Float_t
AliFMDCalibGain
1..n
AliFMDCalibPedestalEntry
#fValue: Float_t
#fWidth: Float_t
AliFMDCalibPedestal
1..n
AliFMDCalibSecondary
#fCorr: TH2D
1
secondary particle correction,
index by η, φ
AliFMDCalibDeadEntry
AliFMDCalibDead
0..n
AliFMDCalibStripEntry
#fDDL: UShort_t
#fChip: UShort_t
#fChannel: UShort_t
AliFMDCalibStrip
1..n
map hardware address
to physical address
AliFMDCalibThreshold
#fValue: Float_t
Used by Poisson recon
algorithm
[Speaker Notes: Next, the pedestal and gain calibrations are read in to translate ADC counts to energy deposition and charge particle multiplicity in each active strip. Given a determination of the primary collision vertex position in (x,y,z), we can calculate the azimuthal angle and pseudorapidity of each strip and the corresponding charge particle multiplicity.]

---
FMD Calibration Data Classes
AliFMDId
#fDetector: UShort_t
#fRing: Char_t
#fSector: UShort_t
#fStrip: UShort_t
AliFMDCalibGainEntry
#fValue: Float_t
AliFMDCalibGain
1..n
AliFMDCalibPedestalEntry
#fValue: Float_t
#fWidth: Float_t
AliFMDCalibPedestal
1..n
AliCDBEntry
AliFMDCalibSecondary
#fCorr: TH2D
TObject
1
secondary particle correction,
index by η, φ
AliFMDCalibDeadEntry
AliFMDCalibDead
0..n
AliFMDCalibStripEntry
#fDDL: UShort_t
#fChip: UShort_t
#fChannel: UShort_t
AliFMDCalibStrip
1..n
map hardware address
to physical address
AliFMDCalibThreshold
#fValue: Float_t
Used by Poisson recon
algorithm
Not Implemented
[Speaker Notes: Next, the pedestal and gain calibrations are read in to translate ADC counts to energy deposition and charge particle multiplicity in each active strip. Given a determination of the primary collision vertex position in (x,y,z), we can calculate the azimuthal angle and pseudorapidity of each strip and the corresponding charge particle multiplicity.]

---
Geometry Classes
Common access to Calibration Data in FMD classes
Ensures all classes uses same data
Simplifies access
Makes client-code type-safe
AliFMDParameters
<<singleton>>
+SetRunNumber(Int_t):void
+SetGainVersion(Int_t v=-1,Int_t s=-1): void
+GetGain(): AliFMDCalibGain
...

---
Conditions DB
Conditions database
These are tied to the DCS, and should be managed by the DCS, but somehow available to calibration and reconstruction code.
Oversampling rate – running the ALTRO faster than pre-amps to sample each strip multiple times.
Strips read out – the number of strips read out can be varied.
Zero suppression – ALTRO can zero suppress data, need to know this to read raw data.
Pedestals – the pedestals subtracted in FEE
Pulser value – for gain calibration

---
Pedestal Calibrations
Calibration Procedures:
Pedestals
DCS: Start
pedestal
calib
`Conditions'
DCS
DB
CDB
LDC
Pedestal
run
Data
PedestalFinder
<<standalone>>
FEE
Possible offline `fixes'
Maps

---
Gain Calibrations
Calibrations Procedures:
Gain & Threshold
DCS
DB
CDB
Find
Threshold
Raw Data
(Low mult.)
Test-beam
Data
Reconstruct
strip ADC counts
Find MPV from
1 (2,3,..) landau(s)
Pulser
data
signal/noise
≈ 60 (QM05)
`Conditions'
Maps
pedestals(?)

---
Calibrations Procedures:
Primary/Secondary Correction
DCS
DB
CDB
Raw Data
Reconstruct
strip ADC counts
Reco Mch ==
Sim Mch?
Reconstruct
energy loss
Propegate
through Sim.
Reconstruct
Mch
Estimate
primary Mch
`Conditions'
Maps
pedestals(?)
Gains
Thresholds
Seed correction

---
Status
Current Status
Class AliFMDParameters serve hard-coded constants to other FMD classes. Should fetch these from DB.
Class AliFMDParameters serve hard-coded constants to other FMD classes. Should fetch these from DB.
Need to implement all calibration procedures.
Need to exercise system of calibration procedures.
Minor: Would like to change AliAltroBuffer ad AliAltroRawStream to handle real ALTRO format.
Question: How does CDB handle looping over many runs? Is run number set centrally?