Use of GEANT4
in ATLAS
Andrea Di Simone
CERN and INFN/CNAF

---
Outline
The ATLAS simulation software
    - Geometry description
    - Job configuration / user interface
    - Misaligned detector
    - Shower parameterization
Computing performance
    - CPU time per event
    - Memory usage @ runtime
    - Eta dependence
    - G4.8.0 tests
    - Automated tests

---
The ATLAS simulation software
Since 2002, the old G3 simulation has been replaced by a new G4-based framework as the official ATLAS simulation software
Fully integrated in the Gaudi-based ATLAS offline framework (Athena)
Used for the simulation of many different setups:
    - Full ATLAS
    - 2004 Combined test beam
    - Stand alone test beams
    - Cosmic commissioning
    - ...

---
The ATLAS simulation software
Used for massive production on the grid:
  - Data challenges
  - CTB production
Features include:
  - G4 geometry built at run time starting from an independent description
  - Choice between different setups done at runtime
    - The same code is used to run all the setups
  - Full job configurability through python scripts

---
Geometry description
The geometrical description of the ATLAS detector is implemented using a dedicated set of classes (GeoModel) with no dependencies on G4
Exactly the same description is used by the reconstruction jobs.
The GeoModel description is built at run time starting from the geometry data bases, and automatically translated to a Geant4 geometry
In spite of the optimizations, the memory usage of the description is quite large:
It is optimized to handle a complex geometry as the one of the ATLAS detector:
number of volumes is kept to the minimum
extensive use of parameterized volumes

---
Geometry description
Pictures obtained using simulation display tools
Toroids
~1000 volumes
Muon chambers:
~451000 volumes
(mostly parameterized)
LAr:
~142500 volumes
(in part parameterized)
Tile:
~8500 volumes
(mostly parameterized)
Pixel:
~6000 volumes
SCT:
~40500 volumes
TRT:
~300000 volumes
(mostly parameterized)

---
Job configuration
All the ATLAS offline software is integrated in a Gaudi based framework (ATHENA)
ATHENA uses the python language as a frontend to the final users
  - a job is controlled via a python script (jobOption)
    - input file(s)
    - which algorithms to run, in what order, with what configuration/parameters
    - output file
The user has all the advantages of a full-featured scripting language
    - flexibility
    - ease of use
    - C++ bindings
G4 has no native interface to python
  - Simulation configuration is normally achieved passing specific command lines to G4
    - several command lines can be grouped in macro files

---
Job configuration
For the simulation of a complex experiment such as ATLAS, the number of G4 macros involved tends to diverge rapidly
  - lack of flexibility
  - maintainability issues
Moreover, the macro based interface does not integrate in the jobOptions mechanism
With the resulting user interface (PyG4Atlas), a simulation job can be controlled and configured (also interactively) from the normal ATHENA prompt
The effort requested to the user in order to interact with the simulation is thus reduced to a minimum
A python layer has been implemented, using bindings to the underlying C++ simulation code, which allows to fully configure a job with python commands

---
Detector misalignments
Detector geometry as installed is of course slightly different from the design one
Need to understand the impact of these misalignments on the physics performance, and include them in both simulation and reconstruction
Misalignment values stored in the geometry DB
  - Retrieved at the beginning of the job using the run number
  - GeoModel uses that info to build the misaligned geometry

---
Detector misalignments
Study done by the Inner Detector:
  - Single electrons, Pt=100GeV
  - Perform misaligned reconstruction on nominal simulation and vice versa
SIMU
RECO
G. Gorfine

---
Detector misalignments
When misaligning both reconstruction and simulation, good physics performance is obtained.
G. Gorfine

---
Detector misalignments
Effect of chamber misalignment on Pt resolution in muon spectrometer
Muon chambers shifted and rotated randomly
M. Schott
1mm shifts
Ideal geometry

---
Shower parameterization
Most of the simulation time is spent for EM showers in the calorimeters
Shower parameterization would allow to speed up this process
  - replace the full simulation of the shower propagation with ad-hoc placement of energy depositions according to parameterized shower shape
Parameterisation used in ATLAS is based on Grindhammer & Peters, arXive:hep-ex/0001020v1h
Work presented in the following slides done by A. Waugh and E. Barberio

---
Shower parameterization
Conditions for parameterization
    - Only electrons/positrons are parameterized.
    - Photons are returned to full sim and the first electron produced is parameterized.
    - Particle must be within allowable energy range, if not it is returned to full simulation
    - Shower must be contained within the calorimeter, checked at Z(95%) and R(95%).
Handling of Leakage
    - If shower not contained, returned to full simulation; when the shower produces a fully contain electron, it is parameterized
Showers starting before the calo
    - Particles are tracked using full simulation until they enter the calo, then each is parameterized separately

---
Shower parameterization
If the conditions are satisfied
  - the track is killed
  - generate fake steps of a chosen length (10m) along the initial electron trajectory; calculate energy deposited and number of spots for each step
  - applying sampling fluctuation, taking into account the calorimeter resolution, calculate energy and position of each spot
  - generate hits and fill fake step to feed the sensitive detector
  - follow the full simulation chain to process the hits
  - loop until the total shower energy is deposited

---
Shower parameterization
EM barrel calo, 10GeV electrons, 1000 events
Full and Fast simulations
Results obtained with analysis at the G4Hit level
Small disagreement on RMOL, still to be clearly understood

---
Shower parameterization
Simulation time for single electrons as a function of the energy
Full and Fast simulations

---
Computing performance
Computing performance is kept under continuous monitoring
  - CPU time per event
    - Measured using different samples, both single particles and full physics events
  - Memory at beginning of first event
    - Contributions from each initialization step are measured
  - Memory at end of run
    - Check the absence of leaks

---
CPU time per event: single particles
Single particle performance well under control since the last big production (~1.5 years ago)
Similar plot available for single muons

---
CPU time per event: physics events
Performance of full physics events is also compatible with the one of release 9.0.4
Some big oscillations are due to problems (fully understood) in the CPU time measurement

---
Memory usage
Memory usage variations observed up to now are not worrying, and are however fully understood
Small problem with g4.8.0.p01 (now fixed)

---
Eta dependence
Users can decide at runtime to limit the simulation only to a certain eta interval
This has a strong impact on performance
G4 ATLAS simulation done by default in the eta range (-6,6)
Older simulation (G3) used to work with a different eta range (-3,3)
A clear understanding of the eta dependence of the simulation time allows to:
    - Identify the regions where most of the CPU time is being spent
    - Better compare performance with the one by G3

---
Eta dependence
Average CPU time per event is measured for different eta intervals using full physics samples.
As expected, the effect is bigger in minimum bias events. This is clearly visible in the lower plot, where the CPU time is normalized to the time needed in -3<eta<3.
Eta dependence
Eta cut
CPU time per event (kSI2K)
Eta dependence
Eta cut
CPUtime(eta)/CPUtime(3)

---
G4.8.0 tests
Several tests done in order to understand the impact on computing performance of the new msc implementation
The same ATLAS simulation software (Athena release 11.5.0) has been built twice, using G4.7.1.p01 and G4.8.0.p01
G4.8.0 was tested with several different configurations:
  - Default: with the new msc and ATLAS standard cuts
  - Special cuts: new msc and 1mm cut for all volumes
  - Msc71: plugging in g4.8.0 the msc implementation from g4.7.1
  - Nsl: same as “Default” but inhibiting the step limitation by the msc

---
G4.8.0 tests
Timing results for full physical events are shown, as obtained in the different configurations. Ratios wrt G4.7.1 timing results are reported as well.

---
G4.8.0 tests
The increase in time is really due only to the new msc implementation, and it is connected with the step limitation
Setting all the production cuts to 1mm does not help in reducing the processing time
In order to have timing results compatible with the ones we used to have with g4.7, we would probably have to choose between
    - Using the old msc implementation
    - Using the new msc implementation, switching off the step limitation

---
Automated tests
RTT (RunTimeTester) is the tool provided by Athena for automated tests of the software functionality
Since last year, it is also used to test the G4 ATLAS simulation:
  - “Fast” tests with single particle samples done for each nightly build
      - Time per event
      - Memory usage at each event
  - Tests using full physical events done at each Athena release
  - Results archived and presented on a web page for easy consultation.

---
Conclusions
The G4 based ATLAS simulation is nowadays fully-featured:
  - Allows detector misalignment
  - Physics validation of shower parameterization ongoing
Its computing performance is continuously monitored:
  - Since the last big production, both CPUtime per event and memory usage remained constant, in spite of the addition of new features
Computing performance tests with G4.8 already done. Physics performance tests ongoing